The George Washington University 
School of Engineering and Applied Science 
Department of Electrical and Computer Engineering 
ECE 001 - LAB 
Homework # 3

Using the light sensor to navigate a circular path

Instructions:  Write an Interactive C program that executes the following set of instructions:

Pseudo-code program:

// initially, robot moves forward (use motor function).

// robot continues moving forward while analog sensor 2 indicates darkness (value > 200)

// robot then turns right while analog sensor 2 indicates brightness (value < 200)

// robot then goes forward again and repeats the process

// by going forward then turning and repeating, robot will navigate the circle indefinitely

Requirements:

- Program must have comments at the beginning, describing the problem overview.

- Program must have comments explaining the general idea of the important aspects of it, i.e. what the digital function does, what port it accesses.  (This does NOT mean put a comment after every line!)

- Hard copy of the program must be submitted at the beginning of the lab, and must be typed, or written in a legible manner.

HINTS: The following commands will be useful:

You will most likely need both the IF statement and WHILE loop construct to complete this program!

motor ( port, speed ) ;

if ( condition ) ;

while ( condition ) ;

ao ( ) ;

analog ( port ) ;

Questions:

Answers to the following questions are intended concise and to be at most 1 to 2 sentences in length.

- What is the difference between an analog sensor and a digital sensor (i.e. what are the values they return)?

- What is the difference between the light sensor and the IR “top hat” sensor?

- What is electromagnetic radiation (list any sources used for this)?

- Do our sensors “sense” electromagnetic radiation?  If so what kind (for the light sensor & the “top hat” sensor)?

Note: Homework is to be done individually and violation of the GWU academic integrity code will be reported to GWU Office of Academic Integrity.

# Text boxes

ROBOT

3

1

LIGHT SENSOR

2

CIRCULAR PATH FOR ROBOT TO FOLLOW

WHEELS