The George Washington University 
School of Engineering and Applied Science 
Department of Electrical and Computer Engineering 
ECE 1020 - LAB 
Homework # 3

Student Name:____________________

Problem #1 Series Circuit Analysis (20 points)

The Battery’s Voltage is: Vs = 6 V

The Resistance of each resistor: R1 = 100 Ω, R2 = 200 Ω, R3 = 300 Ω

Calculate the current along this simple series circuit.

Solution:

I =

(Don’t forget the units…amps, volts, ohms…or the prefix: milli, micro, nano, pico)

Problem #2 Parallel Circuit Analysis(20 points)

The Resistance of each resistor: R1 = 200 Ω, R2 = 300 Ω,

The Current across each resistor: I1 = 60 mA , I2 = 40 mA

Calculate the voltage across each resistor VR1 and VR2.

Calculate the battery’s voltage: Vs?

Solution:

VR1=

VR2=

VS  =

(Don’t forget the units…amps, volts, ohms…or the prefix: milli, micro, nano, pico)

Problem #3 Diode Circuit Analysis(20 points)

The Resistance of each resistor: R0 = 1KΩ

The diode’s threshold voltage is 0.7V (Voltage required to turn the diode “on”).

For a DC voltage of 1.7V, calculate: I1, I2 & the voltage drop across R0 (VR1).

Recalculate the above if the DC source is 0.3V?

Solution:

I1=

I2=

VR0  =

I1=

I2=

VR0  =

(Don’t forget the units…amps, volts, ohms…or the prefix: milli, micro, nano, pico)

Problem #4 Diode Circuit Analysis(20 points)

Using the above resistor values and a DC voltage of 3.7V, calculate the total current flowing through the circuit.

The diode’s threshold voltage is 0.7V (Voltage required to turn the diode “on”).

Solution:

Itotal=

(Don’t forget the units…amps, volts, ohms…or the prefix: milli, micro, nano, pico)

# Text boxes

I1

I2

I2

I1

Itotal